ECEN 449: Microprocessor System Design
Department of Electrical and Computer Engineering
Texas A&M University

Prof. Sunil Khatri
TA: Winfield Wen

Laboratory Report #10

Section 504

Audio Player Application with IR-remote and AC’97 Codec

YAYUN LIU

Dec 4, 2013

Introduction

This lab is to create an application which is capable of playing the wav files stored on the CF card. In order to implement the functionality, the custom device drivers for the IR-remote and AC’97 audio device are needed. The system hardware for this lab is depicted in Figure 1.

Figure 1: Hardware/Software System Diagram

Procedures

    Part1
In the first part, there are two tasks. First, we are required to use a “rising edge” triggered interrupt. Additionally, the transferred data should be from user space to kernel space. We need to write the write routine so that the data movement is from user space to kernel.

Re-import the audio controller peripheral setting both the playback and record interrupts are rising-edge triggered.
1.1. In the "name and version" page, you need to manually input the name and make sure it's exactly the same as that in lab 9.
1.2. In the "source file types" page, check both "HDL source files" and "Netlist files"
1.3. In the "HDL Analysis Information" page, manually add the .vhd files under folder "fifo_coregen"
1.4. In the netlist file page, manually add the files from folder "netlist"
1.5. When you select the interrupt sensitivity type, please click on the playback and record interrupts individually and make the selection individually.
1. The device_write routine. In this routine, get_user() method is used to get data from the user data segment to the kernel data segement. The device driver sleeps using ‘wait_event_interruptible()’ when the audio FIFO is full.
2. In the interrupt_handler, it should only call ‘wake_up_interruptible’ to wake up the write method so that it can continue to transfer data.
3. Crete a devtest application to test if the data from the predefined buffer in “audio_samples.h” is successfully transferred to the audio codec.

Part 2

At this point, we should enable support for audio files which have either one channel or two channels.

1. In the ioctl() routine, cmd used to determine which command users give. When cmd is ENABLE_DISABLE_MONO, if val is false, then mono is disable. Otherwise, if val is true, the mono is set.
2. In the write method, when mono is set to true, duplicate samples are written to the playback FIFO.

     Part 3
        The next step is to create an application which can open an audio file, parse the header within the wav file to determine the format of the file, initialize the audio codec accordingly, and copy data from wav file to the audio device driver file.

1. Use open method to open our audio device file at the beginning of the main function. And then in the open_wav_file() routine, initially open wav file. Use mmap method to map file to region of memory.
2. Ensure we can play wav file, we should make the ‘format’ filed equal to 1 and ‘bits_per_sample’ equal to 8.
3. Next, we should set playback rate utilize the ioctl functionality of the audio device driver.
ioctl(fd_out, ADJUST_PLAYBACK_RATE, setting_ptr2);
Finally, we need to make the audio_samples pointer point to beginning of data section and it points to current sample as well.

Part 4
 Now we need to add the IR-remote to control the wav player application.
1. Create a 200 byte buffer, which is in user space, to read in all messages in queue.
2. After reading in the IR-remote messages, process every message, updating the system accordingly.

Part 5
     The final capability the player application owns is the ability to select various wav files by using certain buttons on the remote.
1. In the while loop, determine if file selection changed load in a new file. Munmap and close the previous file using munmap and close method and then open the new file.
2. If ‘Channel Up’ is pressed, set the channel_up flag and new_file flag to 1. Similarly, when ‘Channel Down’ pressed, set the channel_down flag and new_file flag to 1.

Results

     The seven wav files on the compact flash card could be played accordingly when I press the ‘Channel Up’ button. If the ‘muting’ button is pressed, no sound comes from the speaker. And the ‘pause’ can stop the sound and play at where it left off when I press ‘play’. And ‘Volume Up’ and ‘Volume Down’ buttons can be utilized to control the sound of wav files.

Questions

[a] In your wav player application, we suggested the use of mmap for reading the contents of the wav file. What other ways are there to accomplished the same thing? Compare and contrast these methods. Some of the things to consider include ease of use, code readability, efficiency, and blocking time. Hint: You can find more information on mmap in the O’Reilly’s Linux System Programming book available for free on-line.
      Solution
     An lseek/write implementation can also accomplish the same thing as mmap method does.
A big constraint exists when ISA devices are used on some non-x86 platforms, because their hardware view of ISA may not be contiguous. For example, some Alpha computers see ISA memory as a scattered set of 8-bit, 16-bit, or 32-bit items, with no direct mapping. In such cases, you can’t use mmap at all. However, there are sound advantages to using mmap when it’s feasible to do so. For example, there is a X server, which transfer a lot of data to and from video memory; mapping the graphic display to user space dramatically improves the throughput, as opposed to the lseek/write implementation.
 [b] What is the purpose of the call to ‘madvise’? What might be the effect of removing this call? You can test this with the ‘audio samples7.wav’ which is a full length song recorded at 44100 Hz with two channels (stereo)?
Solution
The madvise() system call advises the kernel about how to handle paging input/output in the address range beginning at address start and with size length bytes. It allows an application to tell the kernel how it expects to use some mapped or shared memory areas, so that the kernel can choose appropriate read-ahead and caching techniques.
      This call does not influence the semantics of the application (except in the case of MADV_DONTNEED), but may influence its performance.
      In this lab, if we remove the call to ‘madvise’, then it can’t play the song continuously. Its performance is not as good as the one when the ‘madvise’ is added.

[c] Why are wav files stored using little-endian byte representation even though the MicroBlaze is a big-endian processor? What are the costs associated with the conversion from little-endian to big-endian in your current application?
Solution
WAV files are little-endian(least significant bytes first) because the format originated for operating system running on intel processor based machines which use the little-endian format to store numbers.
Obviously, the costs associated with the conversion should be time and memory space.

[d] If you wanted to support 16-bit audio in your wav player application, what changes to your existing code would you have to make? Would your audio device driver have to change? If so, how? Hint: Research how 16-bit audio samples are stored in wav files.
      Solution

      If we want to support 16-bit audio, then our audio device driver have to be modified. In the current write routine of the audio device driver, we have a char variable sample_c, and get_user(sample_c, buff) method is to get data from the user data segment to the kernel data segment. Now, if we want to support 16-bit, we should make sample_c a u16 type variable.

Conclusion

This lab exercise familiarized me with the device driver creation in an embedded Linux
environment. What is more, this lab provides me with experience developing drivers that handle buffering of real-time data.

Appendix: C files and Head files

Appendix 1: audio_buffer.c
/* Moved all prototypes and includes into the headerfile */
#include "audio_buffer.h"

/* This structure defines the function pointers to our functions for
   opening, closing, reading and writing the device file. There are
   lots of other pointers in this structure which we are not using,
   see the whole definition in linux/fs.h */
// file operations structure
static struct file_operations fops = {
  .read = device_read,
  .write = device_write,
  .open = device_open,
  .release = device_release,
  .ioctl = device_ioctl,
};

/*
 * This function is called when the module is loaded and registers a
 * device for the driver to use.
 */
int my_init(void)
{

  init_waitqueue_head(&queue); /* initialize the wait queue */

  /* Initialize the semaphore we will use to protect against multiple
     users opening the device */
  sema_init(&sem, 1);

  /* Map virtual address to multiplier physical address */
  printk(KERN_INFO "Mapping virtual address....\n");
  virt_addr = ioremap(PHY_ADDR, MEMSIZE);
  baseaddr = (u32)virt_addr;
  printk("physical address is: 0x%x\nvirtual address is: 0x%x\n", PHY_ADDR, baseaddr);

  Major = register_chrdev(0, DEVICE_NAME, &fops);
  if (Major < 0) {
    printk(KERN_ALERT "Registering char device failed with %d\n", Major);
    return Major;
  }
  printk(KERN_INFO "Registered a device with dynamic Major number of %d\n", Major);
  printk(KERN_INFO "Create a device file for this device with this command:\n'mknod /dev/%s c %d 0'.\n", DEVICE_NAME, Major);

  return 0; /* success */
}

/*
 * This function is called when the module is unloaded, it releases
 * the device file.
 */
void my_cleanup(void)
{
  /*
   * Unregister the device
   */
  unregister_chrdev(Major, DEVICE_NAME);
  /* Unmapping virtual address space */
  printk(KERN_ALERT "unmapping virtual address space....\n");
  iounmap((void*)virt_addr);
}

/*
 * Called when a process tries to open the device file, like "cat
 * /dev/irq_test". Link to this function placed in file operations
 * structure for our device file.
 */
static int device_open(struct inode *inode, struct file *file)
{

  int irq_ret;

  if (down_interruptible (&sem))
    return -ERESTARTSYS;

  // We are only allowing one process to hold the device file open at
  // a time.
  if (Device_Open){
    up(&sem);
    return -EBUSY;
  }
  Device_Open++;

  // OK we are now past the critical section, we can release the
  // semaphore and all will be well
  up(&sem);

  // request a fast IRQ and set handler
  irq_ret = request_irq(IRQ_NUM, irq_handler, 0 /*flags*/ , DEVICE_NAME, NULL);
  if (irq_ret < 0) { /* handle errors */
    printk(KERN_ALERT "Registering IRQ failed with %d\n", irq_ret);
    return irq_ret;
  }

  //initialize AC97
  /*Initialize the codec with or without loopback, this statement could be commented out*/
  XAC97_InitAudio(baseaddr, 0);
  //enables variable rate audio mode (enables sample rate registers and SLOTREQ signaling
  XAC97_WriteReg(baseaddr, AC97_ExtendedAudioStat, 1);
  //set master volume to max
  //XAC97_WriteReg(baseaddr, AC97_MasterVol, AC97_VOL_MAX);
  //set headphone volume to max
  XAC97_WriteReg(baseaddr, AC97_AuxOutVol, AC97_VOL_MAX);
  //set the PCM playback rate at 11025Hz
  XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_11025_HZ);
  //XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_11025_HZ);

  mono = 0;
  try_module_get(THIS_MODULE); /* increment the module use count
        (make sure this is accurate or you
        won't be able to remove the module
        later. */

  printk(KERN_ALERT "Device opened\n");
  printk(KERN_ALERT"IRQ Num %d called\n", IRQ_NUM);
  return 0;
}

/*
 * Called when a process closes the device file.
 */
static int device_release(struct inode *inode, struct file *file)
{
  Device_Open--; /* We're now ready for our next caller */

  // perform a soft reset on the audio codec
  XAC97_SoftReset(baseaddr);

  // unregister the interrupt handler
  free_irq(IRQ_NUM, NULL);

  /*
   * Decrement the usage count, or else once you opened the file,
   * you'll never get get rid of the module.
   */
  module_put(THIS_MODULE);
  printk(KERN_ALERT "Device closed\n");

  return 0;
}

/*
 * Called when a process, which already opened the dev file, attempts to
 * read from it.
 */
static ssize_t device_read(struct file *filp, /* see include/linux/fs.h */
        char *buffer, /* buffer to fill with data */
        size_t length, /* length of the buffer */
        loff_t * offset)
{

/* Fail */
}

/*
 * Called when a process writes to dev file
 */
static ssize_t device_write(struct file *filp, const char *buff, size_t len, loff_t * off)
{

  u32 sample;
  char sample_c;

  while(len)
  {
    /*
     * The buffer is in user data segment, not the kernel segment.
     * We use get_user which gets data from the user data segment
     * to the kernel data segment.
     */
    get_user(sample_c, buff);
    sample = 10*(u32)((unsigned char)sample_c);
    buff++;

    /* sleep when the audio FIFO is full */
    //wait_event_interruptible(queue, XAC97_isInFIFOFull(baseaddr) );

    if(XAC97_isInFIFOFull(baseaddr))
      wait_event_interruptible(queue, 1);

    //XAC97_WriteFifo(baseaddr, sample);
    //XAC97_WriteFifo(baseaddr, sample);
    if(!mono)
    {
      // stereo
      XAC97_WriteFifo(baseaddr, sample);
      XAC97_WriteFifo(baseaddr, sample);
    }
    else
      // mono
      XAC97_WriteFifo(baseaddr, sample);
    len--;
  }
  return 0; /* Fail */
}

/* Just wake up anything waiting for the device */
irqreturn_t irq_handler(int irq, void *dev_id)
{
  wake_up_interruptible(&queue);
  return 0;
}

/* This function allows the user process to provide control
   command to our device driver and read status from the device */

static int device_ioctl(struct inode *inode,
        struct file *file,
        unsigned int cmd,
        unsigned int *val_ptr)
{
  u16 val; //temportary value
  get_user(val, val_ptr); //grab value from user space

  //printk(KERN_ALERT "cmd = %d, val = %d\n", cmd, val);

  // switch statement to execute command
  switch(cmd)
  {

    //enable or disenable mono
    case ENABLE_DISABLE_MONO:
      if(val==0)
        mono=0;

      else if(val==1)
        mono=1;
      break;

    // adjust aux volume
    case ADJUST_AUX_VOL:
      XAC97_WriteReg(baseaddr, AC97_AuxOutVol, val);
      break;

    // adjust playback rate
    case ADJUST_PLAYBACK_RATE:
      if(val==0){

        XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_8000_HZ);
        XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_8000_HZ);
      }

      else if(val==1){

        XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_11025_HZ);
    XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_11025_HZ);
      }

      else if(val==2){

        XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_16000_HZ);
        XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_16000_HZ);
      }

      else if(val==3){

        XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_22050_HZ);
        XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_22050_HZ);
      }

      else if(val==4){

        XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_44100_HZ);
        XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_44100_HZ);
      }

      else if(val==5){

        XAC97_WriteReg(baseaddr, AC97_PCM_DAC_Rate, AC97_PCM_RATE_48000_HZ);
        XAC97_WriteReg(baseaddr, AC97_PCM_ADC_Rate, AC97_PCM_RATE_48000_HZ);
      }
      break;

    // if unknown command, error out
    default:
      printk(KERN_INFO "Unsupported control command!\n");
      return -EINVAL;
  }

  return 0;
}

/* These define info that can be displayed by modinfo */
MODULE_LICENSE("GPL");
MODULE_AUTHOR("Yayun Liu");
MODULE_DESCRIPTION("xac97 driver");

/* Here we define which functions we want to use for initialization
   and cleanup */
module_init(my_init);
module_exit(my_cleanup);

Appendix 2: wav_play.c
#include <sys/types.h>
#include <sys/stat.h>
#include <fcntl.h>
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <sys/mman.h>
#include <unistd.h>
#include <sys/dir.h>
#include <sys/param.h>
#include <dirent.h>
#include <string.h>
#include "parse_wav.c"
/*user defined header files*/

#include "sound.h"

#define SMAPLE_SIZE 4000
#define ENABLE_MONO 1
#define DISABLE_MONO 0
#define AC97_VOL_ATTN_DELTA_DB 0x0101
#define ENABLE_PLAY 1
#define DISABLE_PLAY 0
/*function prototypes*/
static int open_wav_file(char* filename);
static int wav_file_filter(const struct direct *entry);

/*global variables shared by all functions in this source*/
static int fd_out, fd_in;//file designators for audio device and wav file
static int fd_ir; // file designator for ir device
static struct stat file_info;//used for getting file length needed by mmap
int val;//temp variable used for ioctl calls
unsigned int *val_ptr;
static void *contents;//points to the beginning of the mmap region
static unsigned char *audio_ptr;//points to current audio sample
static unsigned char *samples;//points to the beginning of the audio data
static int num_samples;//number of samples in current wav file
//static unsigned short msg_buff[200];//used to hold read IR messages
char msg_buff[200];
/*audio playback mode settings*/
int vol_setting, playback_rate, mono_setting, pr_val; //hold current audio settings
unsigned int *setting_ptr1, *setting_ptr2;
static int play_audio = 0;//play flag
//static int stop_audio = 1;//stop flag
static int completion_mode = 1; //0=stop,1=repeat,2=forward,3=reverse
static int mute_audio = 0;//mute flag
static int channel_up = 0;//channel up flag
static int channel_down = 0;//channel down flag
static int volume_up = 0;//volume up flag
static int volume_down = 0;//volume down flag

static int num=0;
static int new_file = 0;

static unsigned short current_volume = AC97_VOL_ATTN_0_DB;

int main()
{
  int i; //loop variable
  unsigned short user_input;
  int ir_read_bytes, audio_write_bytes;
  int quit = 0; //exit flag
  //counters which handle the multple message problem
  int wait_count = 0;
  struct dirent **namelist;//structure pointer for reading directory
  int num_files; //number of wav files contained in directory
  int cur_file=0; //index points to wav file currently open
  int nxt_file=0;

  unsigned int cmd;
  char buffer[4000];
  //char buffer_ir[200]={0};//a 200 byte buffer in user space
  int result;

  /*scan current directory for wav files and provide them in alphabetical order*/
  num_files = scandir(".", &namelist, wav_file_filter, alphasort);
  if(num_files < 0) //handle errors
  {
    perror("scandir");
      return -1;
  }

  /*open ir device file*/
  fd_ir = open("/dev/irq_test", O_RDWR);
  /*handle error opening file*/
  if(fd_ir<0)
  {
    printf("Failed to open ir device!\n");
    return -1;
  }

  /*open audio device file */
  fd_out = open("/dev/xac97", O_RDWR);
  /* handle error opening file */
  if (fd_out < 0)
  {
    printf("Failed to open ac97 device file!\n");
    return -1;
  }

  // for test
  printf("Before opening\n");

  /*initially open first wav file*/
  /*open and mmap file, check for valid file, and adjust codec*/
  printf("Opening %s\n", namelist[cur_file]->d_name);
  if(open_wav_file(namelist[cur_file]->d_name)<0)
    return -1;//if error opening

  while(quit != 1) //continue until killed
  {

    /*if file selection changed load in a new file*/
    if(nxt_file != cur_file && new_file==1)
    //if( nxt_file != cur_file)
    {
      new_file = 0;
      num = 0;
      //*munmap current mapping*/
      munmap(contents, file_info.st_size);
      /*close currently opened file*/
      close(fd_in);
      printf("Opening %s\n", namelist[nxt_file]->d_name);
      /*open and mmap file, check for valid file, and adjust codec*/
      if(open_wav_file(namelist[nxt_file]->d_name)<0)
        return -1;//if error opening
      /*clear contents already written to audio device*/
      /*update current file index*/
      cur_file = nxt_file;
    }

    printf("play_audio is %d.\n", play_audio);

    /*copy num_samples worth of samples from wav file to
      audio device in repeat mode*/
    //if(play_audio == 1 && stop_audio == 0)
    if(play_audio == ENABLE_PLAY)
    {
      printf("It's playing!\n");
      for(i=0; i< 4000; i++)
      {
        buffer[i] = *audio_ptr;
        num++;
        audio_ptr++;
        if(num==num_samples)
        {
        num=0;
        audio_ptr = samples;
        break;
        }
      }
      //for testing

      write(fd_out, buffer, 4000);
    }

    else // if not writting audio data
    usleep(100000); // sleep for 100ms

    /*read in all messages in queue*/
    read(fd_ir, msg_buff, 4);

    //convert char to int type
    result = (unsigned int)((unsigned char)msg_buff[3])*256*256*256 +
        (unsigned int)((unsigned char)msg_buff[2])*256*256 +
        (unsigned int)((unsigned char)msg_buff[1])*256 +
        (unsigned int)((unsigned char)msg_buff[0]);
    printf("Decoded message : 0x%x\n", result);

    switch(result)
    {

      /*change the volume*/
      //when volume up is pressed
      case 0x92000000:
        printf("volume up\n");
        if(volume_up==0)
        {
        if(current_volume==AC97_VOL_ATTN_0_DB)
        current_volume = AC97_VOL_ATTN_0_DB;
        else
        current_volume = current_volume - AC97_VOL_ATTN_DELTA_DB;
        volume_up = 1;
        }
        else if(wait_count == 0)
        {
        volume_up = 0;
        }
        val = current_volume;
        val_ptr = &val;
        ioctl(fd_out,ADJUST_AUX_VOL,val_ptr);
        break;

      //when volume down is pressed
      case 0x93000000:
    printf("volume down\n");
        if(volume_down==0)
        {
        if(current_volume==AC97_VOL_ATTN_46_0_DB)// the lowest sound
        current_volume = AC97_VOL_ATTN_46_0_DB ;
        else
        current_volume = current_volume + AC97_VOL_ATTN_DELTA_DB;
        volume_down = 1;
        }
        else if(wait_count == 0)
        {
        volume_down = 0;
        }
        val = current_volume;
        val_ptr = &val;
        ioctl(fd_out,ADJUST_AUX_VOL,val_ptr);
        break;

      /*change the channel to switch wav files*/
      //if channel up pressed
      case 0x90000000:
        printf("channel up\n");
        if(channel_up==0)
        {
        /*open next wav file in directory*/
        nxt_file=cur_file+1;
        new_file = 1;
        if(nxt_file==num_files)
        nxt_file=0;//circular nature
        channel_up = 1;
        }
        else if(wait_count == 0)
        {
        channel_up = 0;
        }
        break;

      //if channel down pressed
      case 0x91000000:
    printf("channel down\n");
        if(channel_down==0)
        {
        /*open next wav file in directory*/
        nxt_file=cur_file-1;
        new_file = 1;
        if(cur_file==0)
        nxt_file=num_files-1;//circular nature
        break;
        channel_down = 1;
        }
        else if(wait_count == 0)
        {
        channel_down = 0;
        }

      //when play is pressed
      case 0xdf000000:
    printf("play\n");
        play_audio = ENABLE_PLAY;
       // stop_audio = 0;
        break;

      //when pause is pressed
      case 0xdc000000:
    printf("pause\n");
        play_audio = DISABLE_PLAY;
        break;

      //when stop is pressed
      case 0xde000000:
       // stop_audio = 1;
    printf("stop\n");
        play_audio = DISABLE_PLAY;
        num=0;
        audio_ptr = samples;
        break;

      /*when mute pressed*/
      case 0x94000000:
        /*update codec*/
    printf("muting\n");
        val = AC97_VOL_MUTE;
        val_ptr = &val;
        ioctl(fd_out,ADJUST_AUX_VOL,val_ptr);
        break;

      //when exit is pressed
      case 0xe3000000:
    printf("exit");
        quit = 1;
        break;

      default:
        ;
    }

  /*maintain wait scheme used to ignore multiple messages*/
  if(wait_count>3)
    wait_count = 0;
  else if(wait_count!=0)
    wait_count++;

  for(i=0; i<4; i++)
    msg_buff[i] = 0;

  }

  close(fd_in);
  close(fd_out);
}

/*this function opens a wav file,
  maps its contents to memory, parses
  the wav header, and adjusts the audio
  codec accordingly
*/
static int open_wav_file(char* filename)
{

    wav_properties_t wav_info;

    /*open wave file*/
    fd_in=open(filename,O_RDONLY);
    /*handle error opening file*/
    if(fd_in <0){
        printf("Failed to wave file!\n");
        return -1;
    }

    /*get file info*/
    fstat(fd_in,&file_info);

    /*use mmap to map file to region of memory*/
    //mmap file to contents use flags for read only and shared mapping
    //printf("Mapping wav files\n");
    contents = mmap(0, file_info.st_size, PROT_READ, MAP_SHARED, fd_in, 0);

    //ensure mmap worked properly
    if(contents == MAP_FAILED)
    {
        printf("Error with mmap!\n");
        return -1;
    }

    /*advise the kernel to do read ahead*/
    madvise(contents,file_info.st_size,MADV_WILLNEED);
    //printf("Doing madvise success\n");

    /*get wave file info*/
    if( parse_wav((char*)contents,&wav_info) <0 )
    {
        printf("Invalid file type!\n");
        return -1;
    }

    /*ensure we can play wav file*/
    if(wav_info.format != 1)
    {
        printf("Compressed wav files are not supported!\n");
        return -1;
    }
    if(wav_info.bits_per_sample != 8)
    {
        printf("Only 8-bit audio is currently supported!\n");
        return -1;
    }

    /*calculate the number of samples in file*/
    num_samples = wav_info.num_bytes;//only supporting 8-bit audio

    /*adjust audio properties based on wav file*/
    /*set play mode */
    if(wav_info.num_channels == 1)//if mono
        mono_setting=0;//set mono
    else //if stereo
        mono_setting=1;//reset mono
    //use ioctl to enable or disable mono
    setting_ptr1 = &mono_setting;
    ioctl(fd_out, ENABLE_DISABLE_MONO, setting_ptr1);

    /*set playback rate accordingly*/
    playback_rate = wav_info.sample_rate;
    if(playback_rate==8000)
      pr_val = 0;
    if(playback_rate==11025)
      pr_val = 1;
    if(playback_rate==16000)
      pr_val = 2;
    if(playback_rate==22050)
      pr_val = 3;
    if(playback_rate==44100)
      pr_val = 4;
    if(playback_rate==48000)
      pr_val = 5;
    setting_ptr2 = &pr_val;
    //set playback rate
    ioctl(fd_out, ADJUST_PLAYBACK_RATE, setting_ptr2);

    /* part 2(i) initialize audio buffer pointers*/
    samples = wav_info.audio_samples;//point to beginning of data section
    audio_ptr = wav_info.audio_samples;//points to current sample

    /*set play flag to start playing file*/
    play_audio = ENABLE_PLAY;
    printf("success!\n");
    return 0; //success!
}

/*function used by scandir to filter out all files except
  those with the .wav extension*/
static int wav_file_filter(const struct direct *entry)
{
  if(strstr(entry->d_name,".wav")) //if .wav in filename
    return 1;//true
  else
    return 0;//false
}

Appendix 3: devtest.c
#include <sys/types.h>
#include <sys/stat.h>
#include <fcntl.h>
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include "sound.h"
#include "audio_samples.h"

static unsigned short* sample_ptr = &audio_samples[0];

int main()
{
  int fd;
  int i;
  int input;
  unsigned int cmd;
  unsigned int *val_ptr;
  static int num=0;
  char buffer[NUM_SAMPLES];
  sample_ptr = &audio_samples[0];

  /* open device file for reading and writing */
  /* use "open" to open '/dev/xac97' */
  fd = open("/dev/xac97", O_RDWR);

  /* handle error opening file */
  if(fd == -1)
  {
    printf("Failed to open device file!\n");
    return -1;
  }

  printf("Enter 'v' for adjusting volume, 'f' for adjusting frequency and 'q' to exit.\n");

 while(input != 'q')
  {
    if( input == 'v'){
        input = input;
    printf("Please select the voice level. 0-mute, 1-mid, 2-max.\n");
    scanf("%d",&num);
    val_ptr = &num;
    if(*val_ptr== 0 || *val_ptr==1 || *val_ptr==2)
        cmd = ADJUST_AUX_VOL;
    ioctl(fd, cmd, val_ptr);
    }
    else if( input == 'f'){
    printf("Please select the frequency. 0-5--> slow-fast.\n");
    scanf("%d",&num);
    val_ptr = &num;
    if(*val_ptr==0 || *val_ptr==1 || *val_ptr==2 || *val_ptr==3 || *val_ptr==4 || *val_ptr==5)
        cmd = ADJUST_PLAYBACK_RATE;
    ioctl(fd, cmd, val_ptr);
    }

    else if( input == 'm'){
    printf("Please select the track. 0-stereo, 1-mono.\n");
    scanf("%d",&num);
    val_ptr = &num;
    if(*val_ptr==0 || *val_ptr==1)
        cmd = ENABLE_DISABLE_MONO;
    ioctl(fd, cmd, val_ptr);

    }

    for(i=0; i< NUM_SAMPLES; i++)
    {
        buffer[i] = (char) audio_samples[num];
        num++;
        if(num==NUM_SAMPLES)
        {
        num=0;
        break;
        }
    }

    write(fd, buffer, NUM_SAMPLES);

    input = getchar();

  }

  close(fd);
  return 0;

}

Appendix 4: parse_wav.c
#include "parse_wav.h"

/*microblaze is big endian but wave files are strore
  using little endian so we must reverse byte order*/
void reverse_endian(void *in_ptr, void *out_ptr, int num_bytes)
{
    int i; //loop variable
    unsigned char* in = in_ptr;
    unsigned char* out = out_ptr;

    /*loop over number of bytes*/
    for(i=0; i<num_bytes; i++)
        out[i] = in[(num_bytes-1)-i];
}

/*Extract wave file properties given by *buff.
  Return -1 if the file is not of proper
  format.*/
int parse_wav(unsigned char *buff, wav_properties_t *wav)
{
      /*strings used for file format checks*/
      char riff_str[5] = "RIFF";
      char wave_str[5] = "WAVE";
      char fmt_str[5] = "fmt ";
      char data_str[5] = "data";
      /*points to the next byte in the array*/
      unsigned char* cur_ptr = buff;
      /*temporary variables used to hold fields within file*/
      unsigned int length, byte_rate, tmp;
      unsigned int sample_rate, num_bytes;
      unsigned short format, num_channels,bits_per_sample;

      /*ensure curid wave file*/
      /*the first 4 bytes of wave file should
      contain "RIFF"*/
      if(strncmp((char*)cur_ptr,riff_str,4)!=0)
        return -1;
      cur_ptr = cur_ptr + 4;
      /*the next 4 bytes contains the length
        of the rest of the file*/

#ifdef isBigEndian
        reverse_endian(cur_ptr,&length, 4);
#else
        length =*(unsigned int*) cur_ptr;
#endif

#ifdef printInfo
      printf("length of file %d\n",length);
#endif

      cur_ptr=cur_ptr+4;
      /*next 4 bytes should contain "WAVE"*/
      if(strncmp((char*)cur_ptr,wave_str,4)!=0)
        return -1;
      cur_ptr = cur_ptr + 4;
      /*next 4 bytes should contain "fmt "*/
      if(strncmp((char*)cur_ptr,fmt_str,4)!=0)
        return -1;
      cur_ptr = cur_ptr + 8;
      /*format check complete*/

      /*format field*/
#ifdef isBigEndian
        reverse_endian(cur_ptr,&format,2);
#else
        format =*(unsigned short*)cur_ptr;
#endif

#ifdef printInfo
      printf("format = %d\n",format);
#endif
      cur_ptr=cur_ptr+2;

      /*number of channels field*/
#ifdef isBigEndian
        reverse_endian(cur_ptr,&num_channels,2);
#else
        num_channels = *(unsigned short*)cur_ptr;
#endif
      //printf("Number of channels = %d\n",num_channels);
      cur_ptr=cur_ptr+2;

      /*sampling rate field*/
#ifdef isBigEndian
        reverse_endian(cur_ptr,&sample_rate,4);
#else
        sample_rate = *(unsigned int*)cur_ptr;
#endif

#ifdef printInfo
      printf("Sampling Rate = %d\n",sample_rate);
#endif
      cur_ptr=cur_ptr+4;

      /*byte rate field*/
#ifdef isBigEndian
        reverse_endian(cur_ptr,&byte_rate,4);
#else
        byte_rate = *(unsigned int*)cur_ptr;
#endif

#ifdef printInfo
      printf("Byte Rate = %d\n",byte_rate);
#endif
      cur_ptr=cur_ptr+6;//skip block align for now

      /*bits per sample field (2 bytes)*/
#ifdef isBigEndian
        reverse_endian(cur_ptr,&bits_per_sample,2);
#else
        bits_per_sample = *(unsigned short*)cur_ptr;
#endif

#ifdef printInfo
      printf("Bits per Sample = %d\n", bits_per_sample);
#endif
      cur_ptr=cur_ptr+2;

      /*sanity check*/
      tmp = sample_rate*num_channels*bits_per_sample/8;
      if(byte_rate != tmp)
        return -1;

      /*more sanity checks*/
      /*next 4 bytes should contain "data"*/
      if(strncmp((char*)cur_ptr,data_str,4)!=0)
        return -1;
      cur_ptr = cur_ptr + 4;

      /*next 4 bytes contains the number of data bytes*/
#ifdef isBigEndian
        reverse_endian(cur_ptr,&num_bytes,4);
#else
        num_bytes = *(unsigned int*)cur_ptr;
#endif

#ifdef printInfo
      printf("Number of data bytes = %d\n",num_bytes);
#endif
      cur_ptr = cur_ptr + 4; //point to beginning of data

      /*place parsed values into structure*/
      wav->format = format;
      wav->num_channels = num_channels;
      wav->sample_rate = sample_rate;
      wav->bits_per_sample = bits_per_sample;
      wav->num_bytes = num_bytes;
      wav->audio_samples = cur_ptr;
      /*if we got to this point, the file has been successfully
        parsed!*/
      return(0);
}